## Slide 1: Thinking About EMCOMM CERT Communications Planning S.C. ARES November 2007
D. D. Frydenlund KG6LRP

## Slide 2: Thinking About EMCOMM CERT Communications Planning S.C. ARES November 2007
A One Hour Primer In
Emergency Communications
Planning

## Slide 3: Planning
Failure to Plan is
Planning to Fail

## Slide 4: Communications Discipline Getting the Message Through
Clearly Assigned Responsibility
Established Routes
Interference Plan
Redundancy/Robustness
Established Protocols

## Slide 5: CERT Communications Responsibilities
Team Member
Understand Radio Use
Use Radio Protocols
Control Own Radio
Frequency/Tones
Power

## Slide 6: CERT Communications Responsibilities
Team Communicator
Team Member +
Know Relevant Nets
Set Up Out of Team Comms
Know Comms Protocols
Copy Record Traffic

## Slide 7: CERT Communications Responsibilities
Team Leader
Team Member +
Know Up Line Nets
Know Same Level Nets
Control Team Comms
Know Comms Protocols

## Slide 8: Leadership
The First Job of a Leader is to
LEAD!
The Leader and the Communicator are Normally Different People

## Slide 9: CERT Communications Requirements
Portable
Cheap (Acquire and Operate)
Simple
Rugged/Reliable
Short Range (< 10 Miles)
Typically < 1 Mile

## Slide 10: EMCOMM Communications Layers
Level 1 - State OES Regional EOC to Operational Area (County) EOC
Level 2 - Op Area EOC to Juristictions and Emergency Alert System
Level 3 - Op Area EOC to Mobile Units
------------------------- CERT? --------------------------
Level 4 - Jurisdiction OEC to Internal Units
Level 5 - Jurisdiction Internal Unit Intra Unit Communications

## Slide 11: Primary CERT Communications Needs
Report Status
Request Resources
Receive Direction
Receive Information

## Slide 12: Primary CERT Communications Nets
Team to OpCen (Level 4)
Inter Team (Level 5)
Intra Team (Level 5)

## Slide 13: CERT Communications Characteristics
Team to OpCen
Structured/Formal
Directed Net Likely
Brief
Extended Range
Fixed Channel

## Slide 14: CERT Communications Characteristics
Inter Team
Informal/Conversational
Informal Net Likely
Brief
Shorter Range
Flexible Channel

## Slide 15: CERT Communications Characteristics
Intra Team
Informal/Conversational
Team Leader Moderated
Continuous Chatter
Line of Sight
Fixed Channel

## Slide 16: CERT Communications Environment
Spectrum (Bandwidth) Limited
Heavy Official Need/Use
Heavy “Idiot” Use
Lots of Interference

## Slide 17: CERT Communications Doctrine Response
Use Spectrum (Bandwidth) Wisely
Use Privacy Tones Wisely
Do Not Interfere With Others
Frequency Selection
Lowest Useful Power

## Slide 18: Avoiding Interference
Separation By:
Frequency
Time
Space
Tones (PT or CTCSS)

## Slide 19: CERT Communications Tools
FRS Radio
GMRS Radio
HAM Radio
VHF (2 Meter)
UHF (70 Centimeter)

## Slide 20
FRS Radio/GMRS Radio
The “New” Citizen's Bands
~465 Mhz FM Voice
22 Channels
7 FRS
8 GMRS
7 Shared

## Slide 21
FRS Features
Unlicensed
Very Low Power
Poor Antennas (By Law)
Low Range (Typ < 1 Mile)
Channels 8 – 14 Exclusive

## Slide 22
GMRS Features
Licensed
Low Power
Better Antennas Allowed
Low Range (Typ < 2 Miles)
Channels 15 – 22 Exclusive

## Slide 23
FRS Radio/GMRS Radio
Privacy Tones (PT or CTCSS) on FRS/GMRS Radios are NOT Standardized by Number,
Only by Frequency.
If used: ALWAYS TEST!

## Slide 24
HAM Radio Features
Licensed
Variable Power
Better Antennas
Variable Range (HT < 2 Miles)
Mobile > 10 Miles
Repeater - 10's of Miles
Many Frequencies
Standardized CTCSS Tones

## Slide 25: Avoiding Interference
Separation By:
Frequency
Time
Space
Tones (PT or CTCSS)

## Slide 26: Primary CERT Communications Nets
Team to OpCen (HAM, GMRS)
Inter Team (HAM, GMRS, FRS)
Intra Team (FRS)

## Slide 27: Frequency Assignment
Static
Establishing Contact
High Use
Special Application
Dynamic
Temporary Use
Shared Use

## Slide 28: Special Static Frequencies
Calling Frequencies
Used to Establish Contact
FRS/GMRS Channel 1
HAM 2 Meter 146.52 Mhz
HAM 70 cm 446.0 Mhz
Repeater Pairs
Protected Nets
Calling Frequencies

## Slide 29: FRS/GMRS Recommendations
Calling
Channel 1
Team Assignments
FRS 8 – 14
Shared 2 – 7 (Work Down)
OpArea Assignments
GMRS 15 – 22 (Work Down)

## Slide 30: Avoiding Interference
Separation By:
Frequency
Time
Space
Tones (PT or CTCSS)

## Slide 31: Time Assignment
Fixed Slots by Function
WX Channel “Local on the 8's”
Fixed Rotation
Formal Order of “Turns”
Service Request (By Priority?)
First to Fill the Vacancy

## Slide 32: Avoiding Interference
Separation By:
Frequency
Time
Space
Tones (PT or CTCSS)

## Slide 33
Separation by Space

## Slide 34
Needs Separation by:
Frequency or Tone

## Slide 35: Avoiding Interference
Separation By:
Frequency
Time
Space
Tones (PT or CTCSS)

## Slide 36: Privacy Tones PT or CTCSS
“Subaudio” Tone (~100hz)
Suppress Audio Amplifier if Tone is Absent.

## Slide 37: Privacy Tones PT or CTCSS
Advantages
Masks Non-member Transmissions
Creates Illusion of Non-interence
Disadvantages
Not Possible to Hear if Frequency
Really Open and Free

## Slide 38: Sectorizing High Density Communications
A Space Based Method for Maintaining Minimum Interference When There are Many Mobile Teams.
Many = > Available Frequencies

## Slide 39
1.414
1
1
A
A
Communications Radius
Vs Grid

## Slide 40
A

## Slide 41
A
1
0.7
1
0.7

## Slide 42
Rectangular Pattern, Four Sector
A B C D A B C D A B C D A B C D
C D A B C D A B C D A B C D A B
A B C D A B C D A B C D A B C D
C D A B C D A B C D A B C D A B

## Slide 43
12121212121212
12121212121212
12121212121212
12121212121212
12121212121212
12121212121212
12121212121212
A
A
A
A
A
A
A
A
A
A
A
A
B
B
B
B
B
B
B
B
B
B
C
C
C
C
C
C
C
C
C
D
C
D
D
D
D
D
D
D
D
D
D
C
C
C
C
E
E
E
E
E
E
E
E
E
E
E
E
F
F
F
F
F
F
F
F
F
F
F
F
F
G
G
G
G
G
G
G
G
G
G
G
G
G
B
B
D
Hexagonal Grid, Seven Sectors

## Slide 44
Rectangular Pattern, Eight Sector
A B C D E F G H A B C D E F G H
D E F G H A B C D E F G H A B C
G H A B C D E F G H A B C D E F
B C D E F G H A B C D E F G H A
E F G H A B C D E F G H A B C D
H A B C D E F G H A B C D E F G
C D E F G H A B C D E F G H A B
F G H A B C D E F G H A B C D E

## Slide 45
Rectangular Pattern, Nine Sectors
A B C D E F G H I A B C D E F G H I
D E F G H I A B C D E F G H I A B C
G H I A B C D E F G H I A B C D E F
A B C D E F G H I A B C D E F G H I
D E F G H I A B C D E F G H I A B C
G H I A B C D E F G H I A B C D E F

## Slide 46: Establishing YOUR CERT Plan
Keep
It
Simple
Stupid

## Slide 47: Communications Complexity Progression
Chat
Informal Control
Formal Net(s)
Assigned Frequencies
By Team or Function
By Area
By Area and Team and Function

## Slide 48: Key Questions:
How Many Units (Teams) in OpArea?
How Many Frequencies Available?
How Frequent is the Traffic?
How Time Critical is the Traffic?
What is the Range of the Radio?
How Big is the OpArea?

## Slide 49: Communications Discipline Getting the Message Through
Clearly Assigned Responsibility
Established Routes
Interference Plan
Redundancy/Robustness
Established Protocols

## Slide 50: Typical Intra Team Implications
One FRS Radio Channel (8 – 14)
If Inadequate Range, Go GMRS
Informal Net or Chat Mode
No Privacy Tones
Every Team Member Has a Radio
Every Team Member Hears All

## Slide 51: Typical Inter Team Implications
Assigned or Requested Channel
(GMRS 15 – 22 or HAM)
May Need “Calling Frequency”
Shared Channel 1 or HAM
Informal Net or Chat Mode
Only Team Communicator Has Radio
Only Leader + Communicator Hears

## Slide 52: Typical Team/OES Implications
Assigned Channels
(GMRS 15 – 22 and/or HAM)
May Use “Calling Frequency”
Shared Channel 1 or HAM
Formal (Directed) Net
Only Team Communicator Has Radio
Only Leader + Communicator Hears

## Slide 53: OpCen Comms Team
Monitors Calling Freq(s)
Serves as Net Control
Maintains Record of Traffic
Copies/Sends Formal Traffic
Relays Traffic
May Assign Sub Nets/Frequencies
Controls System Transitions

## Slide 54: Team Communicator
Monitors Calling Freq(s)
Maintains Record of Traffic
Copies/Sends Formal Traffic
Relays Traffic
Negotiates/Establishes Comms Links
Disestablishes Comm Links
Stays Near Team Leader

## Slide 55: FRS/GMRS Recommendations
Calling
Channel 1
Team Assignments
FRS 8 – 14
Shared 2 – 7 (Work Down)
OpArea Assignments
GMRS 15 – 22 (Work Down)

## Slide 56: Thinking About EMCOMM CERT Communications Planning S.C. ARES November 2007